www.SteelWindowsandDoors.com

L10 - 	WINDOWS

318	STEEL WINDOWS AND DOORS:

-	Manufacturer and reference:  Crittall Windows Ltd, Corporate™ 2000 range

-	Generally manufactured in accordance with BS 6510, exclusively designed sections (Patent No. 	93/05514.3) specially formed with continuous weather/vision strip grooves 8mm wide x 1.5 mm deep.  Frame sections are flat-faced for enhanced surface quality of the metal with front-to-back dimension 40mm.

-	Weathertightness:  To BS 6375: Part 1

Exposure category (Design wind pressure): 2000 (Pa)

-	For air permeability, water-tightness and wind resistance data see Table AA

-	Operation and Strength characteristics:  To BS 6375: Part 2

-	Construction:  All frames have welded corners and are flat and square within normal 		manufacturing dimensional tolerances of +/- 1.5 mm.  Intermediate bars will be hot tenon riveted. Multilight frames are constructed with welded butt-on fixed lights or hot tenon riveted intermediate bars. Where frame spans exceed multilight elevation size limits, direct frame to frame couplings are employed.

-	Galvanising: All components including steel attachments, coupling members and 	ancillaries:  hot-dipped after manufacture to BS EN ISO 1461:1999

-	Hinging:  Friction stays concealed within the frame sections.  Hinges are face applied.  		Projecting external easy-clean hinges welded onto outer frames are not available.

-	Glazing details:  Will accept double glazing up to 29mm in thickness.

Ventilator frames have upstand of 17mm providing the minimum edge cover of 12mm for adequate 	protection of sealed units.  Glazing gaskets, and glazing beads present no horizontal ledges on which dust and dirt can gather. Drained and ventilated dry glazing systems to be utilised.  Solid	bedding of glass into glazing compounds - not suitable.

-	Weatherstripping:  Ventilators are pressure equalised and fitted with twin gaskets

(external rainscreen/internal air seal) in a co-extrusion with hot melted adhesive applied.

-	Ironmongery/accessories:  See clause 328.

-	Finish as delivered:  Galvanised or Duralife™ coated (see clause 331) in a range of colours.

325	STEEL WINDOWS AND DOORS:

-	Generally all the foregoing.

-	Manufacturing undertaken in the Crittall factory by directly employed personnel.

-	Design testing, manufacture and installation carried out under Quality Management Systems certified to BS EN ISO.9001

328	IRONMONGERY/ACCESSORIES:

-	Standard provisions:  See Brochure/Binder

-	Standard finishes:  Satin anodised or satin chrome according to fitting.

-	Optional hardware/finishes:  Available, consult Crittall.

331	FINISH COATING

-	Type/reference:  Epoxy free Duralife™ polyester powder coating using Interpon D36 powder to BS 6497

-	Preparation:  Following galvanising, windows are chemically cleaned and pre-treated to provide surface to which powder coating will adhere.

-	Covering:  Minimum 60 microns on all significant surfaces.

-	Colours:  Wide selection available.  See Crittall Colour Selector.

-	Process:  Coating will be undertaken in the same manufacturing plant as the frame fabrication.

552	METAL GLAZED SCREENS:

-	Screen/composite window assemblies are available utilising all Crittall ranges.

-	A full design/advice service is available.

-	Coupling details; consult Crittall.

## Table AA

| TYPE OF OPENING LIGHT | EXPOSURE CATEGORY (Pa) | AIR PERMEABILITY: Not More Than 16m3/h/m JOINT, AT (Pa) | WATER TIGHTNESS: NO LEAKAGE, AT (Pa) | WIND RESISTANCE: NO DAMAGE & ONLY PERMISSABLE DEFLECTION, AT (Pa) |
| --- | --- | --- | --- | --- |
| Corporate™ 2000 |  |  |  |  |
| Side Hung Open Out | 2000 | 300 | 300 | 2000 |
| Top Hung Open Out | 2000 | 300 | 300 | 2000 |
| Horizontal & Vertical Pivot | 2000 | 200 | 200 | 2000 |
| Bottom Hung Open In | 2000 | 300 | 200 | 2000 |
| Side Hung Open In | 2000 | 300 | 200 | 2000 |

North American Supplier: Steel Windows and Doors USA

480 Bunnell Street, Bridgeport, CT 06607

Phone: (203) 579-5157  Fax: (203) 579-5158

Website: www.steelwindowsanddoors.com

E-Mail: sales@steelwindowsanddoors.com