- www.SteelWindowsandDoors.com

L10	WINDOWS

320	STEEL WINDOWS AND DOORS:

-	Manufacturer and reference:  Crittall Windows Limited, Homelight ‘L’™ Residential.

-	Windows - generally manufactured in accordance with BS 6510 F section.

* Doors generally manufactured in accordance with BS 6510, W20 section.

-	Weathertightness:  To BS 6375: Part 1.

Exposure category (design wind pressure): 2000 (Pa).

-	For air permeability, water-tightness and wind resistance data see Table AA

-	Operation and strength characteristics: To BS 6375: Part 2.

-	Construction:  All frames have welded corners and are flat and square within normal manufacturing dimensional tolerances of ± 1.5mm.

-	Galvanising:  All components including steel attachments, coupling members and ancillaries: hot dipped after manufactured to BS EN ISO 1461:1999.

- Glazing details:  Will accept double glazing up to 24mm in thickness (excepting ‘H’ Small Pane and certain ‘N’ & ‘Z’ range casements, see catalogue/brochure/ask for details).  Glazing beads present no horizontal ledges on which dust and dirt can gather.

- Glazing to be 4 mm clear float outer / 16mm Argon filled cavity / 4mm soft coat Low E DG units for compliance with Part L of the Building Regulations

-	Weatherstripping:  Dual fin gaskets in extruded PVC secured by studs clipped into inner frame sections.

-	Ironmongery/accessories:  clause 328.

-	Finish as delivered: Galvanised or Duralife™ polyester powder coated (see clause 331) in a range of colours.

322	STEEL WINDOWS:

-	Manufacturer and reference:  Crittall Windows Limited, Homelight ‘L’™ Reversible.

-	Generally manufactured in accordance with BS 6510, exclusively designed sections for double glazed versions, otherwise F section.

-	Weathertightness:  To BS 6375: Part 1.

Exposure category (design wind pressure): 2400 (Pa).

-	For air permeability, water-tightness and wind resistance data see Table AA.

-	Operation and strength characteristics: To BS 6375: Part 2.

-	Construction: All frames have welded corners and are flat and square within normal manufacturing dimensional tolerances of  ± 1.5mm.

-	Galvanising: All components including steel attachments, coupling members and ancillaries: Hot-dipped after manufacture to BS EN ISO 1461:1999.

-	Glazing details:  Will accept double glazing up to 24mm in thickness.

Glazing beads present no horizontal ledges on which dust and dirt can gather.

-	Weather-stripping: Gaskets complying with BS 4255: Part 1 manufactured from neoprene.

-	Ironmongery/accessories:  Safety catch, storm catch, handle and face applied friction pivots.

-	Finish as delivered:  Galvanised or Duralife™ (see clause 331) in a range of colours.

325	STEEL WINDOWS AND DOORS:

-	Generally all the foregoing.

-	Manufacturing undertaken in the Crittall factory by directly employed personnel.

-	Design testing, manufacture and installation carried out under Quality Management Systems certified to BS EN ISO 9001.

328	IRONMONGERY/ACCESSORIES:

-	Standard provisions: See brochure/binder.

-	Homelight™ range hinges, handle plates, stay pegs and brackets are made of steel and are welded to the frames.

-	Reversible windows are hung on steel friction pivots welded to the frames.

-	Standard finishes: Satin anodised or satin chrome according to fitting.

-	Optional hardware/finishes: Available, consult Crittall.

331	FINISH COATING

-	Type/reference: Epoxy free Duralife™ polyester powder coating using Interpon D36 powder to BS 6497.

-	Preparation: Following galvanising, windows are chemically cleaned and pre-treated to provide surface to which powder coating will adhere.

-	Covering:  Minimum 60 microns on all significant surfaces.

-	Colours:  Wide selection available.  See Crittall Colour Selector.

-	Process:  Coating will be undertaken in the same manufacturing plant as the frame fabrication.

552	METAL GLAZED SCREENS:

-	Screen/composite window assemblies are available using all Crittall ranges.

-	A full design/advice service is available.

-	Coupling details:  Consult Crittall.

Table AA

| TYPE OF OPENING LIGHT | EXPOSURE CATEGORY (Pa) | AIR PERMEABILITY: Not More Than 16m3/h/m JOINT, AT (Pa) | WATER TIGHTNESS: NO LEAKAGE, AT (Pa) | WIND RESISTANCE: NO DAMAGE & ONLY PERMISSABLE DEFLECTION, AT (Pa) |
| --- | --- | --- | --- | --- |
| Homelight™ |  |  |  |  |
| Side Hung Open Out | 2000 | 300 | 200 | 2000 |
| Top Hung Open Out | 2000 | 300 | 200 | 2000 |
| Reversible | 2400 | 300 | 400 | 2400 |

North American Supplier: Steel Windows and Doors USA

480 Bunnell Street, Bridgeport, CT 06607

Phone: (203) 579-5157  Fax: (203) 579-5158

Website: www.steelwindowsanddoors.com

E-Mail: sales@steelwindowsanddoors.com